LEN Editorial for Broadcast Film & Video Issue 233.

Full galvanic isolation of signal and ground paths with LEN

In video feeds galvanic isolation is a critical issue both to avoid signal distortion and the possibility of electric shocks, LEN Galvanic Isolators now provide an effective solution with a range of products suitable for either rack mounting or in-line (portable) applications.
Where a video feed utilises multiple pieces of equipment there is an inherent risk of signal distortion, caused by the equipment痴 grounds having different potentials. In addition, voltage differences can, under certain circumstances, cause electric shocks to those working with the equipment, raising health & safety issues, as well as the more widely considered quality issues.
 These issues do not only impact on video feeds within the broadcast and security/defence sectors, but also feeds from medical diagnostic imaging equipment such as digital X-Ray machines, MRI and CT scanners.
LEN are proven specialists in preventing signal distortion and manufacture a broad range of galvanic ground isolators for 3G/HD/SD SDI video use. These isolators out-perform broadband transformers for SDI signals as there is no distortion of the signal, as well as being suitable for the commonly used ASI streaming data format.
   LEN痴 galvanic ground isolators permit the full bandwidth of the SDI signal to pass, whilst offering input and output impedance of 75 ohms and return loss better than 20dB
   For broadcast, security and defence applications, LEN offer both galvanic ground isolators in encapsulated enclosures (which may be rack-mounted within an accessory panel) as well as inline 'barrels', more suitable for portable applications.
For medical grade applications, LEN have developed a galvanic ground isolator, delivering the higher breakdown voltages (up to 4Kv) often associated with diagnostic imaging equipment.
LEN can be contacted via:
Telephone: +44 (0) 1270 886157
Website: www.len.co.uk

Accompanying Photo:
Caption: LEN galvanic rack mounted isolators

Notes for Editors:
1.A JPEG file of the accompanying image is attached to accompany this release.

2.This release is issued by Temeraire Consulting on Behalf of LEN Ltd, in the first instance please direct all enquiries to Andrew Osman at Temeraire Consulting.
- 07932 607932
- andrewosman@temeraireconsulting.co.uk